## Slide 1: PastaBot: FORCE SENSING FOR pasta packaging automation
Alberto Compagnoni
Luca Inghilterra
Alessandro Monteleone
Smart Robotics - Academic Year 2023/2024
Notes: ALE

## Slide 2: Project Description & Objectives
1. Box Localization
Identify the correct push point based on the collected image
2. Sensing
Sense force through controlled pushing interactions.
3. Sorting
Push the box into the correct disposal bin.
Manipulating object by pushing them, the system sorts pasta boxes based on their mass classification
Designed for use cases where the packaging of different products is standardized
Notes: ALE

## Slide 3: Manipulator
ABB GoFa™ CRB 15000
6 DOF
Revolute Joints
Pushing Tool
6D Force/Torque Sensor attached to the joint 6
Notes: ALE

## Slide 4: Setting
Table: center of the scene
Box: placed in a default position (hypothetically taken by a conveyor/roller belt), with variable mass
Disposal bins: three ones, each one as destination for a different mass item
Fixed Camera: FoV over the table
ABB GoFa™ CRB 15000
Notes: ALE

## Slide 5: Tools
Ros
Gazebo
OpenCV
Python
MoveIt
Notes: ale ROS: framework for robotic applications that allows to create nodes and make them communicate

## Slide 6: System Design: Sequence Diagram

## Slide 7: System Design – ROS Nodes and Topics
object_detector |  | 
Topic | Type | Meaning
/camera/image_raw (S) | Image | Image read from top-view camera
/box/type_topic (S) | String | Classified box type “LIGHT_BOX” “MEDIUM_BOX” “HEAVY_BOX”
/box/initial_point (P) | Point | Initial point where the box is located
/box/side_point (P) | Point | Point at which the robot must apply the second push to the box in order to drop it into the disposal container
force_sensor |  | 
Topic | Type | Meaning
ft_sensor_topic (S) | WrenchStamped | Force and Torque read by sensor
box/initial_point (S) | Point | Initial point where the box is located
box/type_topic (P) | String | Classified box type “LIGHT_BOX” “MEDIUM_BOX” “HEAVY_BOX”
trajectory_planner |  | 
Topic | Type | Meaning
/box/initial_point (S) | Point | Initial point where the box is located
/box/side_point (S) | Point | Point at which the robot must apply the second push
Notes: ALBI

## Slide 8: System Design – Full ROS Graph
Notes: ALBI

## Slide 9: 1. Box Localization
Image Acquisition & Preprocessing
Object Detection by Contour Recognition
Push Point Extraction
Homography
Notes: ALBI

## Slide 10: Image Acquisition & Preprocessing
Image Capture: Collect the image and convert it from ROS format to an OpenCV image
Cropping: Performed on the image to focus on RoI in which boxes are located
Color Filtering: Using color thresholding, segment the dark gray regions that correspond to the box's front face (dim light)
Notes: ALE

## Slide 11: Contour Recognition & Object Detection
Suzuki-Abe algorithm (cv2.findContours)
  Pixel Search:
    Starts by looking for pixels that are part of a contour (usually white pixels in a binary image) and, using neighbors, traces the perimeter of the object, following changes in intensity.
  Hierarchy of Contours:
    The algorithm can also build a contour hierarchy, allowing it to distinguish between outer and inner contours (e.g., holes in an object).
Object selection
  Discard polygons which area is not reasonable
Notes: ALE https://theailearner.com/tag/suzuki-contour-algorithm-opencv/

## Slide 12: Push Point Extraction
Identifying the Push Point
  Located at the center of the box's front face bottom edge
  Initially expressed in pixel coordinates (x, y)
Coordinate Transformation
  Homography matrix converts pixel coordinates to real-world space
  Enables accurate spatial positioning for robotic manipulation
Notes: ALE

## Slide 13: Homography Estimation
D (-1.5, 0.4)
C (1.5, 0.4)
A (0, -0.4)
B (0, 0.4)
Image Points ( Pixel )
World Points ( m )
Mapping
A (192, 790)
B (608, 790)
C (608, 10)
D (192, 10)
Notes: ALBI

## Slide 14: Homography Estimation
We use four pairs of points (image_point, world_point) to find the homography matrix (cv2.findHomography)
is then normalized by dividing each element by
We can then obtain the push point in real-world coordinates:
Notes: ALBI

## Slide 15: 2. Sensing
Initial Push Interaction
Force Measurement
Mass Classification

## Slide 16: Initial Push Interaction
Perform inertia measurement for each object
Position Control Scheme (position_controllers/JointTrajectoryController)
Waypoints:
  HOME_POINT as default home position
  START_POINT located 16 cm along the x-axis before reaching the PUSH_POINT
  PUSH_POINT determined by the object detection module
  END_POINT located 20 cm along the x-axis from START_POINT for a consistent and controlled final displacement
HOME_POINT
START_POINT
START_POINT
STOP_POINT
PUSH_POINT

## Slide 17: Waiting Point
END_POINT
WAITING_POINT

## Slide 18: Force Measurement
Newton's Second Law (F = m • a): proportional to the mass of the object
Newton's Third Law (FEnd effector — Box = FBox - End effector ): while performing the Position Control, the contact between the End effector and the box return a thrust to the sensor equal to the thrust needed for moving the box
Friction force ( f = µ • PBox ): proportional to the mass of the object
A 6D force-torque sensor on the wrist detects the forces applied on the end effector.

## Slide 19: Mass/Force Classification
Since the pushing trajectory for weight measurement occurs under position control and involves a very small displacement (approximately 20 cm), we assume constant average acceleration during the contact.
Therefore we can directly classify the force.
force_sensor node monitors the current position of the end effector, collecting force measurements along the x-axis from the sensor when it enters the force measurement area
As soon as the end effector exits the measurement area, the node calculates the average of the five highest force readings to ensure robustness against potential outliers.

## Slide 20: 3. Sorting
Side point localization
Compute pushing trajectory
Push into disposal bin
To ensure that the box is pushed in the correct disposal bin, we need to perform the following steps:

## Slide 21: Side point localization
Mapping of box type to disposal bin:
  "LIGHT BOX“  frontal disposal bin
  "MEDIUM BOX“  right disposal bin
  "HEAVY BOX”  left disposal bin
The force_sensor node publishes the box_type on the topic box/type_topic.
The object_detector node reads this information, calculates the side_point (the point from which the robot should initiate the second push) based on the initial push_point and the distance the box has traveled due to the push, and then publishes it on the topic box/side_point.
Frontal Bin case
Right Bin case
Left Bin case

## Slide 22: Compute pushing trajectory
When the trajectory planner node receives the side_point, then calculates the target disposal bin location and plans the robot's path accordingly.
If the disposal bin is located in front, the robot simply moves in a straight line.
However, if the disposal bin is on the left or right side, the planner must generate an additional waypoint to ensure the end effector reaches the side_point without colliding with the box.

## Slide 23: Push into disposal bin
Once the trajectory is defined, the robot pushes the box into the correct disposal bin. At this point, it is detected that there are no more boxes on the worktable, so_
the arm return to HOME_POINT;
the box_spawner generates a new one.

## Slide 24: DEMO TIME

## Slide 25
THANK YOU FOR YOUR ATTENTION